## Slide 1: Ch9. Switches, Routers and Firewalls
Naveen Kumar Lekkalapudi

## Slide 2: What to expect?
Storage media
Switches
Routers
Firewalls
Interfaces
Logging

## Slide 3: Storage Media
Types of Storage:
  DRAM (Dynamic Random-Access Memory)
    Volatile, looses memory when power is turned off.
    Stores OS configuration, process memory, routing tables
  CAM(Content Access Memory)
    Very Fast memory to access.
    Used to store MAC tables in switches,
  NVRAM (Non-volatile Random-Access Memory)
    NVRAM retains data when power is turned off.
    Flash memory.
    Used in routers to store OS, boot and startup config files.

## Slide 4: Storage Media
Types of storage:
  Hard Drive:
    Most of Network equipment do not include a hard drive.
    Servers acting as firewall/routers can have drives to store OS, startup config, firewall log and extensive other data.
  Read-only Memory(ROM):
    Permanently store data without modification.
    Can be reprogrammed to store data.
    Normally contains bootloader.

## Slide 5: Switches
Switches are Layer 2/3 devices that connect multiple computers together to form a network.
Unlike hubs, switches isolate traﬃc on diﬀerent switch ports, so that each switch port is a separate collision domain.
Why investigate?
  Sniffs traffic
  Contains MAC tables which map port to computer.
  Attacks which confuse switches

## Slide 6: Switches
Content-Addressable Memory Table
  Used for quick access to MAC tables.
  Volatile and changes quickly
  CAM tables contains evidence of sniffing.

## Slide 8: Switches
Address Resolution Protocol
  The Ethernet Address Resolution Protocol (ARP)2 is designed to dynamically distribute Layer 2 Ethernet addresses to systems on the local subnet.
  In Cisco ASA:
  In linux server:

## Slide 9: Switches
Types:
  Managed –ACL, caching, logging.
  Smart –performance monitoring
  Unmanaged –plug-and-play
Evidence:
  Volatile –CAM,ARP tables, ACL, configs, processor memory
  Persistent –OS image, bootloader, startup configuration
  Off-system –log data, flow data.

## Slide 10: Routers
Routers are (by deﬁnition) Layer 3 devices designed to pass packets between networks.
Why investigate:
  Traffic traverses through router
  Network topology helps!
  Routing tables
Types:
  Enterprise
    Packet filtering, DHCP, NAT, QoS, Logging, monitoring.
    CLI, web, remote console, SNMP.
  Consumer
    Port filtering, DHCP, NAT
  Roll-your-own with *nix! -iptables

## Slide 11: Routers
Evidence:
  Volatile –Routing tables, ARP table, DHCP leases, configs
  Persistent –OS image, bootloader, startup config, access logs and DHCP logs.
  Off-system –exports data through syslog, FTP, TFTP.

## Slide 12: Firewalls
Firewalls are essentially souped-up routers capable of inspecting and ﬁltering traﬃc to a much higher degree.
Why investigate:
  Logs have attempts to break in
  Configuration helps understanding services and their scope.
  Can be modified to collect more

## Slide 13: Firewalls
Types:
  Categories:
    Packet Filters
    Session-layer Proxies
    Application proxies
  Enterprise-class:
    NAT, DHCP, VPN tunneling, logging, Load balancing.
  Consumer-class:
    NAT packet-filtering.
    802.11 interface.
  Roll-your-own with *nix and windows.

## Slide 14: Firewalls
Evidence:
  Volatile
    Interface configs, ACLs, Command history, I/O memory
  Persistent
    Bootloaders, startup config.
  Off-system
    Firewall logs, Access history, backup configs.

## Slide 15: Interfaces
How to get evidence from equipment?
Interfaces secured with username and passwords.
Default passwords published online.
Web Interface:
  Portable
  Easy to manage
  Cannot easily export data.
  Browsing modifies volatile memory

## Slide 16: Interfaces
CLI:
  Can connect using serial cables
  Can do
    List contents of flash memory
    Output CAM and ARP tables

## Slide 17: Interfaces
Remote CLI
  Telnet or ssh
  Same commands as CLI
SNMP (Simple Network Management Protocol)
  Gather info or set configs
  CAMs, ACLs, routing tables, all and all
Proprietary Interface:
  Apple airport
  Cisco VMS, ASDM

## Slide 18: Logging
Forensic investigators may ﬁnd device logs to be useful repositories of evidence relevant to a case.

## Slide 19: Logging
Local Logging
  Virtually all switches, routers, and ﬁrewalls perform some amount of event recording by default, and do so by writing out event logs to whatever local media is available.
  Console  screen –L /dev/ttyUSB0
  Terminal  $script –a logfile.txt
  Buffered  volatile and lost with power
SNMP
  Gather data using Get, GETNEXT and GETBULK

## Slide 20: Logging
Syslog
  Inside interface of Cisco ASA
Authentication, Authorization and account logging
  AAA servers at back end
  All transactions recorded at some level.
  Central accounting database reveals all.